Jig or Sabre Saw Safety

NEVER perform maintenance on any saw without unplugging it first and only if you are 	qualified to do so

NEVER operate this or any saw while impaired in any way

Hair pulled back, no loose jewelry, no loose clothing, no open toe shoes

Area free of debris- 3’ clearance all around

Safety Goggles are a MUST

Ear plugs are a MUST

USE FOR CURVED CUTS, RIP AND CROSS CUT

ALWAYS use correct blade for the type of material and the type of cut you are making

Adjust blade angle for cut

Adjust speed and blade variance as necessary for desired cut

Place fence against board

Align blade with cut

One hand on saw at all times

If needed to stabilize board, place other hand on board out of line of cut

Turn on

Slowly bring blade forward and take nick out of lumber

Push blade back and adjust location if needed

SLOWLY push blade all the way through cut- even slower cutting through knots

When changing catch hand placement, check that hand is out of line of cut

Keeping one hand on saw, release trigger

Keep hand on saw until blade comes to complete stop

If blade jams in lumber, keep one hand on saw and turn off saw immediately-see shop 	supervisor

By signing and dating this document, you acknowledge that you have been educated in the various safety procedures needed to operate this saw safely and efficiently, and are comfortable in using this saw.

_______________________________________________		__________________

Printed Name and Social Security Number					Date

_______________________________________________

Signature

_______________________________________________		__________________

Printed Name of Witness							Date

_______________________________________________

Signature