Tucker Theatre Job Safety

MTSU Department of Theatre • 205 Boutwell Dramatic Arts • Murfreesboro, TN 37132

Personnel Lift Safety

ONLY AUTHORIZED AND QUALIFIED PERSONNEL MAY OPERATE THIS MACHINE!

NEVER perform maintenance on any personnel lift without unplugging it first and only if you are qualified to do so.

NEVER operate this or any personnel lift while impaired in any way.

Transporting the lift-

Platform must be completely empty of tools and debris.

Platform must be fully lowered with outriggers removed and stowed.

To move machine use handles provided on the mast crossbar.

Tilt machine back only when on a flat, firm and level surface.

NEVER ALLOW PERSONNEL IN PLATFORM WHILE YOU ARE MOVING MACHINE!!  (This means you cannot place a person in the lift, take it up and loosen the outriggers so you can push that person around.  Outriggers MUST be in locked in contact with the floor ANYTIME the lift is moving up or down, forwards or backwards!)

Operation of lift-

- NEVER operate this or any other personnel lift without the outriggers locked into place and in secure contact with the floor and unit leveled according to the bubble level indicator on the base frame.  Deliberately overriding the outrigger safety mechanisms will result in expulsion from the theatre.

- NEVER operate this machine on uneven, raked or structurally unsound surfaces.  All four outrigger feet must be in direct contact with the stage surface.  If you are working near the stage edge, do not use shims or extensions to level the outrigger feet.

- Before ascending all pockets must be empty.   Crescent wrench and other tools must be securely attached to your person.  No hand, wrist or neck jewelry, no loose clothing and no open toed shoes may be worn.

- While operating this machine, always look in the direction of machine movement.

- To ascend, platform operator must hold both the “dead man switch” and the up button.  To descend, operator must hold both the “dead man switch” and the down button.

- When platform is raised, all ground personnel must be at least 6 feet away from the platform base.

- Check work area for clearance overhead, on sides and bottom of platform when lifting or lowering platform.

- NEVER USE THE MAST ASSEMBLY TO ENTER OR EXIT THE PLATFORM!

- NEVER STAND ON PLATFORM RAILS, STEPS ORLADDERS TO PROVIDE ADDITIONAL REACH.  Keep feet firmly planted on the platform floor at all times.

- Do not tie off machine to any adjacent structure.

- Do not perform work that will subject unit to horizontal force or create a swaying motion of the platform.

- NEVER dismount from a moving machine.

STUDENTS ARE NEVER ALLOWED TO USE THE LIFTS WHILE ALONE IN THE BUILDING!

LIFTS ARE ONLY TO BE USED UNDER THE DIRECT SUPERVISION OF THE FACILITY MANAGER, MASTER ELECTRICIAN, SHOP FOREMAN OR THE DESIGN FACULTY.

By signing and dating this document you acknowledge that you have been educated in the various personnel lift procedures needed to operate this lift safely and are comfortable in using this personnel lift.

_______________________________________			______________________

Printed name and last four digits of SS#				Date

_______________________________________

Signature

_______________________________________			_________________________

Witness								Date