Circular Saw Safety

NEVER perform maintenance on any saw without unplugging it first and only if you are 	qualified to do so

NEVER operate this or any saw while impaired in any way

Hair pulled back, no loose jewelry, no loose clothing, no open toe shoes, no backless

shoes.

Area free of debris- 3’ clearance all around

FOR RIP CUT and CROSS CUT

CUT MUST BE A STRAIGHT LINE ONLY

Safety Goggles are a MUST

Ear plugs are a MUST

Adjust blade height- 1/8” deeper than wood surface

Make certain boards are on stable saw horses or on protected deck

Make certain fence is flush with board

Align saw blade while blade is free of board

Keep both hands on saw or one hand on saw and one on board

Make certain that hands are free of blade path

Turn on

Slowly push saw forward keeping fence flush with board surface

SLOWLY push saw through lumber- even slower cutting through knots

Always keep blade guard down, except when aligning blade

When blade is clear of lumber, turn saw off

If saw must be turned off prior to end of cut, back-track ¼” prior to turning saw off

If saw must be turned on in middle of cut, back-track ¼” prior to turning saw on

Attend saw until blade comes to complete stop

If blade jams in lumber, keep one hand on lumber and turn off saw immediately-see shop 	supervisor

By signing and dating this document, you acknowledge that you have been educated in the various safety procedures needed to operate this saw safely and efficiently, and are comfortable in using this saw.

_______________________________________________		__________________

Printed Name and Social Security Number					Date

_______________________________________________

Signature

_______________________________________________		__________________

Printed Name of Witness							Date

_______________________________________________

Signature