Panel Saw Safety

NEVER perform maintenance on any saw without unplugging it first and only if you are 	qualified to do so

NEVER operate this or any saw while impaired in any way

Hair pulled back, no loose jewelry, no loose clothing, and no open toe shoes

Area free of debris- 3’ clearance all around

Safety Goggles are a MUST

Ear plugs are a MUST

FOR SHEET LUMBER CUTS ONLY

Place board flush against bottom rollers

Vertical Cuts

Align blade to cut line or set sheet at desired measurement using measuring tape

KEEP ONE HAND ON LUMBER AND THE OTHER ON SAW.

Turn on

Slowly pull saw down and take a nick out of lumber, adjust lumber if needed

SLOWLY pull saw down all the way through the lumber, even slower cutting through

knots

Turn saw off

Attend saw until blade comes to complete stop

Retract blade

If blade jams in lumber, keep one hand on lumber and turn off saw immediately-see shop 	supervisor

Horizontal Cuts

Align blade to cut line or set blade at desired measurement and lock in place

Rotate saw for a horizontal cut and lock in place

KEEP HANDS ON BOTH SAVED AND EXCESS(“TRASH”) LUMBER AT ALL

TIMES

Turn on

Slowly push lumber forward and take a nick out of lumber, adjust blade if needed

With hands on the saved and excess lumber, slowly push lumber forward keeping it flush

with rollers

Push lumber all the way through blade having the catcher pull lumber all the way through

blade

If used by one person: Push lumber as far as you can

Back lumber up ¼”, switch sides

Pull lumber the rest of the way through blade

When lumber is clear of blade, turn the saw off

Attend saw until blade comes to a complete stop

If blade jams in lumber, keep one hand on lumber and turn off saw immediately-see shop 	supervisor

By signing and dating this document, you acknowledge that you have been educated in the various safety procedures needed to operate this saw safely and efficiently, and are comfortable in using this saw.

_______________________________________________		__________________

Printed Name and Social Security Number					Date

_______________________________________________

Signature

_______________________________________________		__________________

Printed Name of Witness							Date

_______________________________________________

Signature