Tucker Theatre Job Safety

MTSU Department of Theatre • 205 Boutwell Dramatic Arts • Murfreesboro, TN 37132

Table Saw Safety

NEVER perform maintenance on any saw without unplugging it first and only if you are 	qualified to do so

NEVER operate this or any saw while impaired in any way

Hair pulled back, no loose jewelry, no loose clothing, no open toe shoes

Area free of debris- 3’ clearance all around

Safety Goggles are a MUST

Ear plugs are a MUST

FOR RIP CUT ONLY(unless using a miter fence)

4’ boards or less= 1 man job.  Over 4’= must use a ‘catcher’ or roller table

If cut is less than 3x width of blade cover, MUST use a wood/shark push stick

Adjust blade height- 1/8” above wood surface

Set fence at cut measurement-Use provided tape measure or measure from inside blade

tip to fence

Make certain blade guard is down and aligned

Turn on dust collector

Turn saw key on and wait for green light

Turn the saw on

Place board against fence and against table surface

KEEP HANDS ON BOTH SAVED AND EXCESS LUMBER AT ALL TIMES

Slowly push lumber forward keeping it flush with fence and table surface

SLOWLY push lumber through blade- even slower cutting through knots

When end arrives at blade cover, use shark if necessary

Push lumber completely through blade and free of back of blade cover

When lumber is clear of blade cover, turn saw off

Attend saw until blade comes to complete stop

If blade jams in lumber, keep one hand on lumber and turn off saw immediately-see shop 	supervisor

By signing and dating this document, you acknowledge that you have been educated in the various safety procedures needed to operate this saw safely and efficiently, and are comfortable in using this saw.

_______________________________________________		__________________

Printed Name and Social Security Number					Date

_______________________________________________

Signature

_______________________________________________		__________________

Printed Name of Witness							Date

_______________________________________________

Signature